## Slide 1
Guided By :- Prof. Ankit V Sata
Prof. Ravi K Paragda
Topic Name :PRESSURE GAUGE

## Slide 2: Student Name
)

## Slide 3: Boiler mountings
Boiler mountings are the machine components that are mounted over the body of the boiler itself for the safety of the boiler and for complete control of the process of steam generation.
Various boiler mountings are as under: 1) Pressure gauge 2) Water Level Indicator 3) Fusible plug 4)Safety Valve i) Lever Safety Valve ii) Spring Loaded safety Valve 5) Steam stop valve 6) Feed check valve 7) Blow off cock

## Slide 4
BOILER MOUNTINGS
2. PRESSURE GAUGE
Records gauge pressure
Elliptical spring tube is also called Bourdon tube and is made up of special quality Bronze.
Plug (P) is provided for cleaning the siphon tube.
Siphon is filled with cold water to prevent the hot steam entering into the bourdon tube and spring tube remains comparatively cool.

## Slide 5: PRESSURE GAUGE
Function:
1.To record the steam pressure at which the steam is generated in the boiler.
2. A bourdon pressure gauge in its simplest form consists of elliptical elastic tube bent into an arc of a circle
3. This bent up tube is called as BOURDON’S tube.
4. One end of tube gauge is fixed and connected to the steam space in the boiler. The other end is connected to a sector through a link.

## Slide 6: Working of pressure gauge
When high pressure steam enter elliptical tube , the tube section tends to become circular which causes the end of the tube to move outward.
The movement of the close end of the tube is transmitted and magnified by the link and sector.
The sector is hinged at a point of a link.
The magnitude of the movement is indicated by the pointer on the dial.

## Slide 7: Pressure Measurement
Pressure is the force exerted per unit area
Pressure is the action of one force against another force. Pressure is force applied to, or distributed over, a surface. The pressure P of a force F distributed over an area A is defined as P = F/A

## Slide 8
Pressure Measurement Terms
Absolute Pressure
Measured above total vacuum or zero absolute. Zero absolute represents total lack of pressure.
Atmospheric Pressure
The pressure exerted by the earth’s atmosphere. Atmospheric pressure at sea level is 14.696 psia. The value of atmospheric pressure decreases with increasing altitude.
Barometric Pressure
Same as atmospheric pressure.
Gauge Pressure
The pressure above atmospheric pressure. Represents positive difference between measured pressure and existing atmospheric pressure. Can be converted to absolute by adding actual atmospheric pressure value.
Differential Pressure
The difference in magnitude between some pressure value and some reference pressure. In a sense, absolute pressure could be considered as a differential pressure with total vacuum or zero absolute as the reference. Likewise, gauge pressure (defined above) could be considered as Differential Pressure with atmospheric pressure as the reference.

## Slide 9: Pressure Instruments
Types of Pressure Instruments
Pressure Gauges (Vacuum, Compound, Absolute, Gauge)
Differential Pressure Gauge
Pressure Switch (Vacuum, Absolute, Gauge)
Differential Pressure Switch
Pressure Transmitter (Vacuum, Absolute, Gauge)
Differential Pressure Transmitter
PRESSURE GAUGE
PRESSURE SWITCH
DIFFERENTIALPRESSURE TRANSMITTER

## Slide 10: Pressure Gauge

## Slide 11: Pressure Gauge
Measuring Principle
Bourdon tube measuring element is made of a thin-walled C-shape tube or spirally wound helical or coiled tube. When pressure is applied to the measuring system through the pressure port (socket), the pressure causes the Bourdon tube to straighten itself, thus causing the tip to move. The motion of the tip is transmitted via the link to the movement which converts the linear motion of the bourdon tube to a rotational motion that in turn causes the pointer to indicate the measured pressure.
Coiled Bourdon
Helical Bourdon
“C” Type Bourdon

## Slide 12: Differential Pressure Gauge
Measuring Principle:
Differential pressure gauges have two inlet ports, each connected to one of the volumes whose pressure is to be monitored.
In cases where either input can be higher or lower than the other, a bi-directional differential range should be used.

## Slide 13: Pressure Gauge - Accessories
Pulsation Damper (Adjustable Snubber)
Threads on to a gauge socket and provides a restriction by means of a pin, which may be placed in either of five different sized holes, and thus allows the user to vary the amount of dampening to suit requirements. The pulsating pressure moves the pin up and down, providing self cleaning action.
Safety Glass Front
Safety Glass is normally used to prevent the glass shattering in the event of the bourdon tube rupturing.
Liquid Filled Gauge
The liquid filling is used to dampen any vibration/pulsation in the bourdon, either silicone oil or glycerin is used.
Snubber
Used for dampening and filtering and reducing the damaging effects of pulsation on a gauge. The snubber has a metal disc available in standard grades of porosity.

## Slide 14: Pressure Gauge - Accessories
COIL PIPE
PIG TAIL
Pressure Limit Valve
Protects pressure instruments against surges and pulsations. Provides automatic positive protection and accurate, repeatable performance. Automatic pressure shut-off, built in snubber enhances instrument protecting performance.
Siphon Tubes
Used to dissipate heat by trapping condensed liquid to keep high temperature steam or condensing vapor from damaging the pressure gauge.