## Slide 1
Water Conveyance System
Group members
NIRAV JAYANTIBHAI DHANDHUKIA
SHELADIA MIHIRKUMAR KISHORBHAI
NAIR VIDYA SIVADASAN
Branch - Civil
Guide – Dorin Parmar
Shankersinh Vaghela Bapu Institute of Technology
(075)

## Slide 2
•
Water Conveyance System
Water Conveyance System
• Canals-Canals are the structure constructed to
carry or transport water from the reservoir to
the area which is to be irrigated
• Conduits- A pipe is close conduits used to carry
water under pressure.
Canals
Conduits

## Slide 3
Canals
• Classification of canal
• Classification based on source of supply
i) Permanent Canal
ii) Inundation canal
Permanent canal is one which is fed by a
permanent source of supply
Inundation canal usually draws supplies
whenever there is flood

## Slide 4
• Classification based on function
• Irrigation canal- carries water to
agriculture fields
• Feeder canal- feeds another canal
• Navigation canal- provides navigation
facilities

## Slide 5
• Classification based on origin of canal in a
canal network
• Main canal-carries water from reservoir
• Branch canal- when a main canal reaches area to
be irrigated it gets divided into branches joining
different parts of the area
• Major distributary- these are small canals taking
off from branch canal it supplies water to outlet
• Minor distributary-this are small channels
supplying water to water courses for irrigation
• Field channels-from this channels, water enters
into the field of cultivator

## Slide 6
Canal network
Branch Canal
Major
distributory
Minor
distributory
Field Channel
Field
Channel
Head regulator
Main Canal
Cross
regulator

## Slide 7
• CLASSIFICATION BASED ON ALIGNMENT
• Contour canal-In this alignment the canal generally
follows a
contour except for
necessary slopes.
• Main canal runs as
a contour canal
• Contour canal requires
Cross drainage works
Besides this it can
irrigate on one side only

## Slide 8
• Ridge canal- The canal aligned along natural
watershed is known aas ridge canal.
• It irrigates on both sides, C.D. works can be
avoided

## Slide 9
• Side long canal- In this alignment canal is
across contour
• No cross drainage
works are required

## Slide 10
Canal regulation works
• The structure constructed to regulate the flow into
the canal network are called as canal regulators
• 1) Canal head regulator The structure constructed to
divert the water from the reservoir into the Main
canal is called as Head regulator
• Function of head regulator is to control the entry of
water from reservoir
• To control the entry of silt
• To serve as a meter for measuring discharge

## Slide 14
• Cross regulator:- A regulator constructed into
the main canal or parent canal u/s of the
branch canal so as to control the entry of
water in branch canal is called as cross
regulator.
• Canal Escape:- Irrigation structures
constructed to escape water from the canal
into some natural drain is called canal escape

## Slide 15
Canal Escape

## Slide 16
• Fall and rapids:-
• Fall or rapids are located on the d/s side of the
channel. It becomes necessary to lower the
bed level of canal when the slope of the
ground is steeper than gradient or slope of the
canal.
• Fall:- A fall is structure constructed across a
canal to permit lowering down its water level
and dissipate the surplus energy by falling
water.

## Slide 18
Fall

## Slide 19
Vertical Drop Fall

## Slide 20
• Rapids:- A rapid is a structure constructed to
permit lowering of water level by providing a
sloping ramp of some length this sloping ramp
is called Rapid.

## Slide 22
Cross drainage works
• Irrigation structures constructed for carrying
the canal water safely over or under the
drainage water are called as cross drainage
works.
• When a canal is taken off from the reservoir it
meets various natural drainages so cross
drainage works are required to be constructed

## Slide 23
Aquaduct
• The irrigation structure constructed for
passing canal water safely over the drainage
water is called an aquaduct
• Aquaduct are constructed in following
situations
• Drainage is more as compared to canal water
• The bed of the canal is sufficiently above the
high flood level in the drain.

## Slide 25
Aquaduct

## Slide 26
Syphon Aquaduct
• When high flood level of drain is much higher
above the canal be, the drain is then syphon
i.e. the bed of the drain is depressed below the
crossing.

## Slide 29
Super passage
• When the drainage water is taken over the
canal, the structure is called super passage. It
is just reverse of aquaduct.

## Slide 30
Drainage water
Superpassage

## Slide 31
• Syphon superpassage:- In this case the
canal bed is depressed and ramp is provided
at the exit
• Drainage bed level is at higher lower than full
supply level of canal

## Slide 33
Syphon super passage

## Slide 34
Level crossing
• When canal bed level and drain bed level are
practically the same, drainage water is
allowed to intermingle with the canal water
• Such type of works is known as level crossing.

## Slide 36
Inlet and out let
• Inlet is provided in the canal to admit drain
water into it.
• It is provided in following situations
• Drain water is less in magnitude
• Drain water is free from heavy silt
• The drainage bed level is lower than F.S.l

## Slide 37
Outlet
• It is possible to escape out same quantity of
water through some outlet nearby d/s. out let
is provided on the bank of canal to dispose off
excess water admitted in the canal through
inlet.

## Slide 38
Water conduit
• A pipe is a close conduit, generally circular in
c/s used to carry water under pressure.

## Slide 40
•Thanks