## Slide 1: Elementary Concept of DC circuit
Department of Electrical Engineering
BY:- PARMAR VAISHALI B
PATEL DARSHAP G
PATEL DHVANI C
RANA BRIJESH M
TRIVEDI STAVAN S
Guided by: PROF. (DR.) A.R. CHUDASAMA
NIDHI.J.GOHIL

## Slide 2: Electrical Circuits
We want to transfer electrical energy to perform a task
  We want to supply energy to some load
Charged particles want to “move” when an emf applied
  Apply emf and constrain the path of the charged particles
  Force charged particles to supply energy to the load in order to do work (no path through load  no useful work done!)

## Slide 3: Types of Circuit Elements
Circuit components are generally classified as control elements, passive elements, and active elements
  Control Elements – direct and modify the current (e.g. switches)
  Passive Elements – total energy delivered to the element by the rest of the circuit is nonnegative (e.g. resistors, capacitors, inductors)
  Active Elements – can provide energy to the circuit (e.g. batteries, generators, current, voltage)

## Slide 4: Passive circuit elements - resistors
Circuit symbol: Voltage-current relation (Ohm’s Law)
R is the resistance
  Units are ohms ()

## Slide 5: Passive circuit elements – capacitors
Circuit symbol:
C is the capacitance
  Units are Farads (F)
Voltage-current relation:
Capacitors can store energy

## Slide 6: Passive circuit elements - inductors
Circuit symbol:
L is the inductance
  Units are Henries (H)
Voltage-current relation:
Inductors can store energy

## Slide 7: Types of power supplies
Power supplies can be modeled in a number of ways:
  Voltage, current sources
  Independent, dependent sources
  Ideal and non-ideal sources

## Slide 8: voltage sources:
There are 2 kinds of voltage sources:
Independent voltage sources
Dependent voltage sources, of which there are 2 forms:
  Voltage-dependent voltage sources
  Current-dependent voltage sources

## Slide 9
The schematic symbol that we use for independent voltage sources is shown here.
This is intended to indicate that the schematic symbol can be labeled either with a variable, like vS, or a value, with some number, and units. An example might be 1.5[V]. It could also be labeled with both.

## Slide 10: Voltage Sources – Schematic Symbols for Dependent Voltage Sources
The schematic symbols that we use for dependent voltage sources are shown here, of which there are 2 forms:
  Voltage-dependent voltage sources
  Current-dependent voltage sources

## Slide 11: current sources:
There are 2 kinds of current sources:
Independent current sources
Dependent current sources, of which there are 2 forms:
  Voltage-dependent current sources
  Current-dependent current.

## Slide 12
The schematic symbols that we use for current sources are shown here.
This is intended to indicate that the schematic symbol can be labeled either with a variable, like iS, or a value, with some number, and units. An example might be 0.2[A]. It could also be labeled with both.

## Slide 13: Current Sources – Schematic Symbols for Dependent Current Sources
The schematic symbols that we use for dependent voltage sources are shown here, of which there are 2 forms:
  Voltage-dependent voltage sources
  Current-dependent voltage sources

## Slide 14: Fundamental Laws of Electrical circuit
Ohm’s Law
Kirchhoff’s Law

## Slide 15: Ohm’s Law:
A resistor is a two terminal circuit element that has a constant ratio of the voltage across its terminals to the current through its terminals.
The value of the ratio of voltage to current is the defining characteristic of the resistor.

## Slide 16
A resistor obeys the expression:
where R is the resistance.
If something obeys this expression, we can think of it, and model it, as a resistor.
This expression is called Ohm’s Law. The unit ([Ohm] or [W]) is named for Ohm, and is equal to a [Volt/Ampere].
IMPORTANT: use Ohm’s Law only on resistors. It does not hold for sources.

## Slide 17
THANK YOU