## Slide 1: Swaminarayan college of engineering and technology
Topic: Lighting Scheams And ITS designs
Prepared by: Vani Kiran Guide By:
        Manu P Vinay Jigna Parmar
        Patel Saurabh
        Singh Avinash
        Chavda Bihag

## Slide 2: LIGHTING SCHEAMS
Different Lighting Scheams are :-
1. Direct Lighting
2. Semi- Direct Lighting
3. Indirect Lighting
4. Semi- Indirect Lighting
5. General Lighting

## Slide 3: Direct Lighting
In this the light is directly made to fall on the working plane. If proper reflectors are used then about 80-90% of the total light is made to fall on the working plane.

## Slide 4: Semi- Direct Lighting
In this semi-direct reflectors are used. As a result 60-90% of the total light flux is made to fall on the working plane and the remaining light is used to illuminate the ceiling and wall.

## Slide 5: Indirect Lighting
In this lighting scheame more than 90% of the total light flux is thrown upward to the ceiling for diffuse riflection by usin inverted or bowl reflectors.

## Slide 6: Semi-Indirect Lighting
In this lighting scheame 60-90% of the total light flux is thrown upward to the ceiling for diffuse riflection and remaining light reaches the working plane directly.

## Slide 7: General Lighting
The basic requirment of general lighting is to obtain uniform diffused and glare free lighting. This can be obtained by fluorescent lighting.

## Slide 8: Different Lighting Scheams
CLASSIFICATION | Approximate Light Distribution up wards | Approximate Light Distribution down wards
Direct | 0-10% | 90%-100%
Semi-direct | 10%-40% | 60%-90%
indirect | 90%-100% | 0-10%
Semi-indirect | 60%-90% | 10%-40%
General | 40%-60% | 40%-60%

## Slide 9: Design Of Lighting Schemes
The various factors which should be considered while designing a lighting scheme:-
1. Illumination Level: Illumination level should be sufficient for different locations to avoid glare and shadows.
2. Uniform Illumination: Lighting scheme for particular location should provide uniform illumination as far as possible.

## Slide 10
Thank You