## Slide 1
HASMUKH GOSWAMI COLLEGE OF ENGINEERING
BRANCH :- ELECTRONICS & COMMUNICATION

## Slide 2: Topics
Types Of Cable
Types Of Wiring
Types Of Switches
Industrialing & domestic wiring
SUBJECT : ELEMENTS OF ELECTRICAL
ENGNEERING

## Slide 3: Types of cables
Cables Are Classified Mainly According To :
(1) Conductor Used (2) Types Of Insulation
(3) Voltage Grading (4) Number Of Cores.
The Various Conducting As Well As Insulating Materials Which Can Be Used Have Been Mentioned Earlier.
The Cables Are Divided Into Two Groups Based On The Voltage Grading : (1) 250/440 V Cables And (2) 650/1100 V Cables.

## Slide 4
Depending upon the number of stands, cables are classified as two core, three core, three and a half core and four core cables or even more.
In three and half core cable as well as four core cable there are three stands of equal cross sectional area for R, Y and B phases respectively.
Multi strand cables are more durable. They are more flexible and hence are easier to handle.

## Slide 5
As compared to single core cables, multi core cables have more surface area and therefore their cooling or heat radiating capacity.

## Slide 6: Types of wiring
Wooden casing and capping wiring
CTS (Cabtyre Sheathed Wire)
Cleat wiring
Lead sheathed wire
Conduit wiring

## Slide 8: (1) Wooden casing and capping wiring :-
Such wiring is carried out in grooves of wooden casing.
The casing is made of seasoned teak wood and is used in rectangular blocks having a number of grooves equal to the number of wires.

## Slide 9
Such type of wiring is used for voltage upto 250 V.
It is necessary to safeguard it against dampness and risk of fire.

## Slide 10: (2) CTS (Cabtyre Sheathed Wire) :-
Such a type of wiring used in residences uses cabtyre sheated wire as the conductor.
These wires are run on teak wood battens which in turn are fixed on the walls or, ceiling by means of screws and wooden plugs.

## Slide 11: They have a better appearance as compared to the wooden casing and capping wiring.

## Slide 12: (3) Cleat wiring :-
Such type of wiring is used for taking a temporary connection.
Here vulcanized Indian rubber or polyvinyl chloride insulated wires are used as conductors.

## Slide 13: There are grooves provided on the cleat base to accommodate the wires.

## Slide 14: (4) Lead sheathed wire :-
The conductors used here are insulated with vulcanized indian rubber.
Then, an outer sheath made of lead – aluminium alloy containing 95% lead and 5% aluminium is used to cover the insulated conductor.

## Slide 16: This sheath protects the wiring from mechanical injury, atmospheric action and dampness.

## Slide 17: (5) Conduit wiring :-
The conductors used here are insulated with polyvinyl or vulcanized indian rubber.
They are then carried in mild steel tubes commonly called conduits.
They are concealed inside the plaster of the wall and hence the appearance of the house or the building remains unaffected.

## Slide 18
It provides protection against fire hazards, mechanical damage, dampness and shocks.

## Slide 19: Types of switch
Toggle switch
Push button switch

## Slide 20: (1) Toggle switch :-
It has a projecting arm which moves through a small are thus causing the circuit contacts to either open or close.
From fig. , it can be seen that as the arm moves from the OFF to the ON position through the arc it closes the contacts of the electric circuit.

## Slide 21: Such simple toggle switches are used in most of the houses.More complex toggle switches are also used which may have more than two positions and may open and close more than one circuit simultaneously.

## Slide 22: Types of Toggle Switches :

## Slide 23: (2) Push button switch :- :
Such a switch closes the circuit when pressed and when released, comes back to its original position.
These are commonly used in the doorbell switches, dimmer switches on the automobile head lights etc.

## Slide 24: INDUSTRIAL WIRING
The wiring in the industries and factories should be done according to the Indian electricity rules.

## Slide 26: Factory / Godown lighting circuit
From the wiring diagram , it can be seen that, there are two way switches on the switch boards SB2,SB3,&SB4.
While moving in the godown he can put on lamp L1 by operating the first two-way switch board SB1.
When he reaches the switch board SB2,he can operate the first two-way switch on SB2.

## Slide 27
Thus lamp L2 will be connected between the phase & the neutral & will become ON. L1will become OFF.
Again when he reaches the switch board SB3, he can operate the first switch on SB3 thus putting OFF L2 & putting on L3 & soon.

## Slide 28: Thank You