## Slide 1: Narnarayan Shastri Institute of Technology, Jetalpur A presentation on Magnetic Circuit
Guided By
Priyanka Modi
Lecturer
NSIT, Jetalpur
Prepared By
Shah Mansi
Mehta Umangi
Shah Vrund

## Slide 2: Content
Magnetic Field.
Magnetic Flux.
Magnetic Flux Density.
Magnetomotive force.
Magnetic field intensity.
Permeability.
Reluctance.
Permiance.
Reluctivity.
Magnetic circuit.
Similarities of magnetic and electric circuits.
Dissimilarities of magnetic and electric circuits.

## Slide 3: Magnetic Field
In the region surrounding a permanent magnet there exists a magnetic field, which can be represented by magnetic flux lines similar to electric flux lines.
Magnetic flux lines differ from electric flux lines in that they don’t have an origin or termination point.
Magnetic flux lines radiate from the north pole to the south pole through the magnetic bar.
The strength of a magnetic field in a given region is directly related to the density of flux lines in that region.

## Slide 4
If unlike poles of two permanent magnets are brought together the magnets will attract, and the flux distribution will be as shown below.

## Slide 5
If like poles are brought together, the magnets will repel, and the flux distribution will be as shown.

## Slide 6
If a nonmagnetic material, such as glass or copper, is placed in the flux paths surrounding a permanent magnet, there will be an almost unnoticeable change in the flux distribution.
If a magnetic material, such as soft iron, is placed in the flux path, the flux lines will pass through the soft iron rather than the surrounding air because the flux lines pass with greater ease through magnetic materials than through air

## Slide 7
The direction of the magnetic flux lines can be found by placing the thumb of the right hand in the direction of conventional current flow and noting the direction of the fingers (commonly called the right hand rule).

## Slide 8: Magnetic Flux
Magnetic flux is total number of magnetic lines of force in magnetic field.
It is denoted by Φ
The SI unit for flux is Weber(Wb)
1 Wb = 108 magnetic lines.
Magnetic flux lines do not have physical existence.
Magnetic flux lines never intersects.

## Slide 9: Magnetic flux density
It is defined as magnetic flux per unit area of cross section at right angle to the flux.
It is denoted by B.
Its unit is Tesla(T) or Wb/m2
Flux density is also known as magnetic induction.

## Slide 10: Magnetomotive force
It is the cause for producing magnetic flux in magnetic circuit.
mmf of a coil is equal to the product of number of turns of the coil(N) and current(I) flowing through the coil.
It is denoted by F.
Its unit is Ampere Turns(AT).
        F= NI

## Slide 11: Magnetic Field Intensity
It is defined as the mmf per unit length of magnetic circuit.
It is denoted by H.
Its unit is ampere turn per meter (AT/m).
H=F/l

## Slide 12: permeability
If cores of different materials with the same physical dimensions are used in the electromagnet, the strength of the magnet will vary in accordance with the core used.
The variation in strength is due to the number of flux lines passing through the core.
Magnetic material is material in which flux lines can readily be created and is said to have high permeability.
Permeability () is a measure of the ease with which magnetic flux lines can be established in the material.

## Slide 13
Materials that have permeability slightly less than that of free space are said to be diamagnetic and those with permeability slightly greater than that of free space are said to be paramagnetic.
Magnetic materials, such as iron, nickel, steel and alloys of these materials, have permeability hundreds and even thousands of times that of free space and are referred to as ferromagnetic.

## Slide 14
Permeability of free space 0 (vacuum) is
The ratio of the permeability of a material to that of free space is called relative permeability.

## Slide 15: Reluctance
It is a measure of the opposition offered by a magnetic circuit to the establishment of magnetic flux.
It is defined as ratio of mmf to the flux.
Reluctance = m.m.f/ flux.
It is denoted by S.
The unit of reluctance is AT/Wb.
It is analogous to resistance in electric circuit.

## Slide 16: permeance
It is defined as reciprocal of reluctance.
It is measured of ease with which the flux can be set up in the magnetic circuit.
It is denoted by Ʌ(Lambda).
It unit is Wb/A or Henry(H).
Ʌ = 1/S.

## Slide 17: Reluctivity
It is defined as the reluctance offered by a magnetic circuit of unit length and unit cross-section.
It is also known as specific resistance.
Its unit is meter/henry.
It is analogous to resistivity in electric circuit.
Reluctivity = 1/μ.

## Slide 18: Magnetic Circuit
It is defined as the path followed by magnetic flux.
Magnetic circuit usually consist of magnetic material having high permeability.
In this circuit, magnetic flux start from the point and finishes at same point after the completing path.

## Slide 19: Similarities between magnetic and electrical circuits
Magnetic Circuit
The closed path for magnetic flux is known as magnetic circuit.
M.m.f
Flux
Flux density
Relucance
Reluctivity
Permiance
Permiability.
Electrical Circuit
The closed path for electric current is called electric circuit.
E.m.f
Current
Current Density.
Resistance.
Resistivity.
Conductance.
Conductivity.

## Slide 20: Dissimilarities between magnetic and electrical circuits
Magnetic Circuit
The magnetic flux does not actually flow in the circuit but actually sets up in the magnetic circuit.
For magnetic flux, there are no perfect magnetic insulator.
Energy is required to establish a flux and not to maintain it.
Reluctance does not cause a waste of energy.
Electrical Circuit
Electric current actually flows in the electrical circuits.
For electrical current there are large number of insulator like glass, air and rubber.
Energy required so long as current flows
Resistance cause a waste of energy