## Slide 1: MANUFACTURE OF PORTLAND CEMENT
Presented By:-
Students: Naisargi Shah
Surbhi Singh
Faculty name: Patel dipsa
Institute name: Food procrssing technology department
A.D.patel institute of technology
Karamsad

## Slide 2: RAW MATERIALS
Calcareous material
Argillaceous materials
Powdered coal or fuel oil
Gypsum

## Slide 3: Functions of ingredients
Lime- principle constitute; excess or lesser amount reduces strength of cement
Silica-impart strength to the cement
Alumina- make cement quick setting , excess amount weakens the cement
Calcium sulphate- retards setting action
Iron oxide- for colour, strength, hardness to the cement

## Slide 4
Sulphur trioxide-imparts soundness to cement;excess reduces soundness of cement
Alkalis-causes cement efforescent if present in excess

## Slide 5: MANUFACTURE
It happens in two steps:-
Mixing process- (a)dry process
(b)wet process
Burning

## Slide 6: Mixing
Dry process
Raw materials(limestone and clay) are crushed.
Each separate powdered ingredient is stored in a separate hopper.
Powdered material are mixed in the required proportion to get dry ”raw mix” which is stored in storage bins and kept ready to be fed in a rotary kiln.

## Slide 7
Wet process
The calcareous raw materials are crushed, powdered and stored in a big storage tank.
The basin washed clay is also stored.
From the channel the two raw materials are led to “grinding mills” where they are mixed intimately to form a paste called slurry.
The slurry is led to a “correcting basin”
The slurry contains about 30-40% water.
The slurry is finally stored in a storage tank and kept ready for feeding to a rotary kiln.

## Slide 8: Burning
Rotary kiln- dimensions: 90-120 m long, 2.5-3 m diameter.
The kiln is slightly inclined and supported on roller bearing.
The kiln is capable of rotating at 1 RPM about its longitudinal axis .
Maximum temperature is about 1750⁰C

## Slide 9
PROCESS
The raw mix OR corrected slurry is injected into the kiln at its upper end while hot flames are forced into the kiln from the lower end.
Due to slope and slow rotation of the kiln, the materials move towards the lower end (hottest end) at the speed of about 15 m per hour.

## Slide 10
CHEMISTRY
At 400C water evaporates from the slurry(drying zone)
At 1000C decomposition of limestone to form lime(calcination zone)
At 1500-1700C lime and clay undergo chemical interaction or fusion yielding calcium aluminate and silicates(clinkering zone)

## Slide 11
The aluminates and silicates then form small, hard greyish stones called clinkers
These clinkers are very hot .
The kiln is provided with another small rotary kiln at the base.
In it hot clinkers fall and cool air is admitted from opposite side due to which the clinkers cool and are collected in small trolleys.
Hot air thus produced is used for burning powdered coal/oil.

## Slide 12: Grinding
The cooled clinkers are ground to a fine powder in ball mills and tube mills.
During final grindings, a small quantity of powdered gypsum is added.
This additions increases the settling time of the cement.
Gypsum acts as a retarding agent for early setting of cement.

## Slide 13: packing
The ground cement is stored in silos from which it is automatically fed into the packing machines.
Each bag contains 50 kgs of cement

## Slide 14: Disadvantages of rotary kiln
It can only be used for large cement plants involving large capital investments

## Slide 15: THANK YOU