## Slide 1: Overview of An Engineering Graphics
Prepared by
Degama Kishan (130540106024)
Goti Satishkumar
(130540106038)
Dalsaniya Mahek (130540106023)
Kaneriya Yash (130540106056)
Guided By
Prof. Piyush B. Patel
Mechanical Engg. Dept.
Darshan Institute of Engg. And Tech., Rajkot

## Slide 2
TOPICS
Traditional Drawing Tools
Orthographic projection
Graphics language
Engineering drawing
Orthographic projection

## Slide 3: GRAPHICS LANGUAGE

## Slide 4
1. Try to write a description of
this object.
2. Test your written description
by having someone attempt to make a sketch from your
description.
Effectiveness of Graphics Language
The word languages are inadequate for describing the size, shape and features completely as well as concisely.
You can easily understand that …

## Slide 5
Graphic language in “engineering application” use
lines to represent the surfaces, edges and contours of objects.
A drawing can be done using freehand, instruments or computer methods.
Composition of Graphic Language
The language is known as “drawing” or “drafting” .

## Slide 6
Freehand drawing
The lines are sketched without using instruments other than pencils and erasers.
Example

## Slide 7
Instrument drawing
Instruments are used to draw straight lines, circles, and curves concisely and accurately. Thus, the drawings are usually made to scale.
Example

## Slide 8
Computer drawing
The drawings are usually made by commercial software such as AutoCAD, solid works etc.
Example

## Slide 9: Engineering Drawing

## Slide 10
Elements of Engineering Drawing
Engineering drawing are made up of graphics language
and word language.
Graphics
language
Describe a shape (mainly).
Word
language
Describe size, location and specification of the object.

## Slide 11: Traditional Drawing Tools

## Slide 12
DRAWING TOOLS

## Slide 13
1. Drawing Board
2. Mini Drafter
DRAWING TOOLS

## Slide 14
3. T-Square
4. Triangles
DRAWING TOOLS

## Slide 15
5. Adhesive Tape
6. Pencils
2H or HB for thick line
4H for thin line
DRAWING TOOLS

## Slide 16
7. Protector
8. Scale
DRAWING TOOLS

## Slide 17
9. Roller Scale
10. French curve
DRAWING TOOLS

## Slide 18
11. Sandpaper
12. Compass
DRAWING TOOLS

## Slide 19
13. Pencil Eraser
14. Erasing Shield
DRAWING TOOLS

## Slide 20
15. Circle Template
16. Drawing Clip
DRAWING TOOLS

## Slide 21
17. Sharpener
18. Clean paper
DRAWING TOOLS

## Slide 22: PROJECTION METHOD

## Slide 23
PROJECTION THEORY
The projection theory is based on two variables:
1) Line of sight
2) Plane of projection (image plane or picture plane)
The projection theory is used to graphically represent
3-D objects on 2-D media (paper, computer screen).

## Slide 24: PROJECTION METHOD
Perspective
Oblique
Orthographic
Axonometric
Multiview
Parallel

## Slide 25
Line of sight is an imaginary ray of light between an
observer’s eye and an object.
Line of sight
Parallel projection
Line of sight
Perspective projection
There are 2 types of LOS :
parallel
converge
and

## Slide 26
Plane of projection is an imaginary flat plane which
the image is created.
The image is produced by connecting the points where
the LOS pierce the projection plane.
Parallel projection
Perspective projection
Plane of projection
Plane of projection

## Slide 27: Disadvantage of Perspective Projection
Perspective projection is not
used by engineer for manu-
facturing of parts, because
1) It is difficult to create.
2) It does not reveal exact
shape and size.
Width is distorted

## Slide 28: Orthographic Projection

## Slide 29: MEANING
5
Orthographic projection is a parallel projection technique
in which the parallel lines of sight are perpendicular to the
projection plane
Object views from top
Projection plane
1
2
3
4
5
1
2
3
4

## Slide 30: ORTHOGRAPHIC VIEW
Orthographic view depends on relative position of the object
to the line of sight.
Two dimensions of an
object is shown.
Three dimensions of an object is shown.
Rotate
Tilt
More than one view is needed
to represent the object.
Multiview drawing
Axonometric drawing

## Slide 31
Orthographic projection technique can produce either 1. Multiview drawing that each view show an object in two dimensions.
2. Axonometric drawing that show all three dimensions of an object in one view.
Both drawing types are used in technical drawing for communication.
NOTES
ORTHOGRAPHIC VIEW

## Slide 32
Axonometric (Isometric) Drawing
Easy to understand
Right angle becomes obtuse angle.
Circular hole becomes ellipse.
Distortions of shape and size in isometric drawing
Advantage
Disadvantage
Shape and angle distortion
Example

## Slide 33
Multiview Drawing
It represents accurate shape and size.
Advantage
Disadvantage
Require practice in writing and reading.
Multiviews drawing (2-view drawing)
Example

## Slide 34
Methods of Drawing Orthographic Projections
First Angle Projections Method
Here views are drawn
by placing object
in 1st Quadrant
( Fv above X-y, Tv below X-y )
Third Angle Projections Method
Here views are drawn
by placing object
in 3rd Quadrant.
( Tv above X-y, Fv below X-y )
FV
TV
X
Y
X
Y
G
L
TV
FV
SYMBOLIC
PRESENTATION
OF BOTH METHODS
WITH AN OBJECT
STANDING ON HP ( GROUND)
ON IT’S BASE.
NOTE:-
HP term is used in 1st Angle method
&
For the same
Ground term is used
in 3rd Angle method of projections

## Slide 35
S.V.
F.V.
V.P.
P.P.
FOR T.V.
FOR S.V.
FOR F.V.
OBJECT
FIRST ANGLE
PROJECTION
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE
SITUATED IN FIRST QUADRANT
MEANS
ABOVE HP & INFRONT OF VP.
OBJECT IS INBETWEEN
OBSERVER & PLANE.
ACTUAL PATTERN OF
PLANES & VIEWS
IN
FIRST ANGLE METHOD
OF PROJECTIONS
X
Y
VP
HP
PP
FV
LSV
TV

## Slide 36
FOR T.V.
FOR S.V.
FOR F.V.
P.P.
V.P.
F.V.
S.V.
OBJECT
IN THIS METHOD,
THE OBJECT IS ASSUMED TO BE
SITUATED IN THIRD QUADRANT
( BELOW HP & BEHIND OF VP. )
PLANES BEING TRANSPERENT
AND INBETWEEN
OBSERVER & OBJECT.
ACTUAL PATTERN OF
PLANES & VIEWS
OF
THIRD ANGLE PROJECTIONS
X
Y
TV
THIRD ANGLE
PROJECTION
LSV
FV

## Slide 37
Basic Line Types
Types of Lines
Appearance
Name according
to application
Continuous thick line
Visible line
Continuous thin line
Dimension line
Extension line
Leader line
Dash thick line
Hidden line
Chain thin line
Center line
NOTE : We will learn other types of line in later chapters.

## Slide 38
Visible lines represent features that can be seen in the
current view
Meaning of Lines
Hidden lines represent features that can not be seen in the current view
Center line represents symmetry, path of motion, centers of circles, axis of axisymmetrical parts
Dimension and Extension lines indicate the sizes and location of features on a drawing

## Slide 39
Example : Line conventions in engineering drawing

## Slide 40
Thank You